## Slide 1: Acausality A single component for all causalities
Conductor
The resistance R is set
The voltage v is known
 The current i is the solved for
Resistor
The resistance R is set
The current i is known
 The voltage v is the solved
Same model
The resistor illustrates well the principle of acausality.
And it is true for all models.
It does not mean that all causalities are desired – there are ways to influence the causality selection.

## Slide 2: Bi-causality All variables known to compute the parameter value
The current i is set as initial equation
The voltage v is known
 The resistance R is the solved for
In Modelica, a model results in two problems to solve: the initialization problem and the time simulation problem.
Here we leverage the former to compute the value of R and reuse the computed value for time simulation.
R is the solved for in this equation
For this problem, R is found to be 10,5 Ohm.
This value is used for the time simulation to determine the value of the current trajectory.